## Slide 1
Name: Shrey Shah
Designation: Researcher
Institution: OPMG/MESA
Project Title: Design of novel Actuator for coarse and fine; range & resolution
MAJOR OBJECTIVES:
Determine components of Actuator assembly along with working of various sub-assemblies and parts used in them.
Selection of Gears, their modules, ratios and material to put in use in the assembly. Motor to be selected simultaneously.
Designing of Fine stage flexure, determining the reduction ratio to be kept. Variation of parameters affecting the reduction ratio, determining optimal tolerances to be given when fabricating. Testing of a prototype flexure to verify its working.
METHODOLOGY FLOW CHART:
RESULTS/MAJOR FINDINGS:
Actuator assembly and working finalized with rough dimension.
Sub-assemblies to be used: Camshaft assembly, Tumbler mechanism and ballscrew mechanism.
Working of each gear pass from motorhead to camshaft to tumbler mechanism to ballscrew.
Gear dimensions, module and material was finalized based on size and strength considerations.
Sensors compared and selected: LVDT for coarse movement and Capacitive Probe for fine movement.
Modelling of fine stage flexure for reducing eccentric shaft movement.
Variation of parameters to filter those having higher impact on reduction ratio.
Thickness of inner sections and angle of those sections play a
crucial role in determining the reduction ratio.
Tolerances decided based on above procedure; for fabrication.
Fabrication of a sample flexure and testing of the same.
CONCLUSION:
Gears were selected for transfer of power and motion in various parts. Using gears as a reduction mechanism and gearhead of motor, very high reduction was achieved. FSF was successfully designed and modelled for RR with tolerances that do not compromise range and resolution of the actuator.
Guide: Shri. Sahil Patel
Contact e-mail: spatel@sac.isro.gov.in
01 JUN 2022 to
15 AUG 2022
SRTD-RTCG-MISA
Need for Actuator
Design Mechanism
Determining Components
Gear Selection
Motor Selection
Gear Pass calculations
Bearing Selection
Sensor type Selection
Fine Stage Flexure modelling
Parameter variation
Result comparison
Determining Tolerances
Fabrication and testing
End